## Slide 1: Material Flow Analysis Fundamentals
Lecture (II): Procedures, Application & Perspectives

## Slide 2: Lecture (II): Procedures, applications & perspectives
❶ General context – Why using Material Flow Analysis?
❷What is Material Flow Analysis?
❸ How to carry out a Material Flow Analysis?
  General procedure
  Illustrative case study: Global aluminium cycle
❹ Perspectives & conclusions
  Other types of MFA according to OECD
  Other sustainability tools
  Summary of the lecture
Index

## Slide 3: Lecture (II): Procedure, Application & Perspectives
❸ How to carry out a Material Flow Analysis ?
  ̶ General procedure

## Slide 4: MFA procedure
Define the objectives and parameters to be monitored
Limit the balance scope
Limit the balance period
Identify and define the process steps
Draw the flowcharts: material flows – quality
Draw up the balances: material flows – quantity
Interpret the results and draw conclusions
Source: United Nations Industrial development Organization (UNIDO)
Goal & Scope
Quantification
Interpretation

## Slide 5: MFA is an iterative process !
Source: Practical Handbook of Material Flow Analysis, Brunner P.H. & Rechberg H. (2004)
Problem definition / Research question
Goal & Scope
adjustment
Selection of substances
Determination of system boundaries
Determination/ selection of processes
Determination/selection of goods
Determination of flows and stocks
Illustration & interpretation
Determination of mass flows
Balancing the goods
Determination of concentration
Balancing of substances
Adjust system
Redefine problem
1. Refine concentrations
1. Refine
mass flows
2. Re-determine goods
2. Refine mass flows

## Slide 6
❸ How to carry out a Material Flow Analysis ?
    ̶ Illustrative case study: the global Aluminum cycle
Lecture (II): Procedure, Application & Perspectives

## Slide 7: Problem definition / Research question
“ The purpose of this study is the quantification of regional stocks and flows of rolled, extruded and casting alloys across space and over time, giving the industry the ability to evaluate the potential to recycle aluminium scrap most efficiently.”
Sources: Asland aluminium, creative commons
Goal & Scope

## Slide 8: Selection of goods & substance
Targeted substance: Aluminium
Al
13
26,98
Goods:
  Primary Aluminium
  Recycled Aluminium
  Alumina
  Bauxite
  New and old scrap
  Alloys
  Semi-finished casting products (ingots)
  Final products
↘ All flows are expressed in Aluminium mass equivalent value
(for Bauxite & Alumina: mass ratio of Aluminium to other constituents)
Goal & Scope

## Slide 9: Spatial and Temporal Boundaries
Spatial: Nine regional models representing Worldwide scale
Temporal: 1950 – 2017 with a particular focus on the year 2014 in the paper
Goal & Scope
see: http://www.world-aluminium.org/statistics/massflow/
Region | Countries | Comments
China | Mainland China | Important ingot producer &consumer of final products
Europe | EU28+others | Covering regional Europe not only political union
Japan | Japan | Excellent data quality – High per capite consumer of final products
North America | Canada, Mexico, USA | Important ingot producer and co nsumer of final products. Mexico recycles a lot of scrap from USA
Middle east | Arabic peninsula + Iran | Important primary ingot producer. High per capita consumer of final products
Other producing countries | Autralia, Azerbadjan, Russia, South Africa… | Large bauxite, alumina and primary producing regions
South America | Argentina, Brazil, Venezuela, etc. | Covering bauxite mine and high income countries in the South America
Rest of the World | All other countries | No bauxite, alumina or primary aluminium producers. Importer of semis and final products

## Slide 10: Selection of processes
Goal & Scope
Bauxite mining
Alumina production
[Mining & Refining]
Primary production
Recycled production
[Aluminium production]
Semi-fabricated product manufacture (rolling, extrusion, casting, others
[Fabrication]
Stock of product in-use
[Use]
Production of final products
[Manufacturing]
Management of EOL products
New scrap
[Scrap recovery & Trading]
Short exercise:
List several flows & stocks to be quantified in the system

## Slide 11: Identification of flows and stocks
Goal & Scope
Flows:
  All the flows between the processes (linking the 6 main stages)
  Inter-regional trade (Import/Export of metal & final non-metal products)
  Extraction of bauxite in each region
  Emission of residues & waste (not recycled)
Stocks:
P1: Stocks of bauxite and Alumina (Alumina refineries, ports, storage facilities)
P3: Aluminium ingot stock
(Aluminum production)
P6: Final product in use
(Anthropogenic stock)
P8: Disposal - landfill & incineration
(Anthropogenic stock)
P9: Bauxite stock change [extraction] (economic reserve is out of the scope)
P10: Residue wastes, metal losses during manufacturing

## Slide 12: Draw the flowcharts: material flows – quality
Goal & Scope
World scale = Σ Regional Scales
Region, year
Mining & Refining
Aluminum Production
Fabrication
Manufacturing
Scrap recovery & trading
Use
Other regions
Non-metal flows
Metal flows
Alumina
Lithosphere
Disposal & Residue
Disposal & Incineration
P9
P10
P8
P1
P3
P6
Ingots
Semis
Final products
EoL Products
Bauxite
Bauxite
Alumina
Residues
Metal loss
Alloys
Ingots
Semis
Final products
Other uses
Final products
Used products
New & old scrap
Not recycled
New & old scrap
Fabrication scrap
New scrap

## Slide 13: Draw up the balances: material flows (Worldwide scale)
All flows are expressed in Aluminium mass equivalent value (in million tonnes)
Stock in 2014 equals stock in 2013 plus the stock change in 2014
Inconsistency in the mass balances
Quantification

## Slide 14: Data reconciliation with STAN sofware
Measurements and estimates are subject to errors (e.g. inconstancies in the law of mass conservation)
Data reconciliation statistically adjusts the values to resolve contradictions and find the data that fit the model the best
Most probable value (A) with associated uncertainty (b) is calculated:
Quantification
A ±b

## Slide 15: Recycling rates
Metal-specific recovery rate =
Recycled content of ingots flow
Interpretation

## Slide 16: Comparison between the regions in 2017 (China / Europe / Rest of the world)
Quantification
http://www.world-aluminium.org/statistics/massflow/
Bauxite
Alumina + scrap
Ingots
Semis
Final Products
EoL Products
New + Old
scrap
Old
scrap

## Slide 17: Comparison of Bauxite & Alumina flows in 2017 (China / Europe)
Quantification
http://www.world-aluminium.org/statistics/massflow/
China | Europe
Refining input: 39,9 Mtonnes of Bauxite (67% domestic – 32% import) | Refining input: 4 Mtonnes of Bauxite (4,4% domestic – 95,6% import)
Output: 35,6 Mtonnes of Alumina (total ouputs: 89% Alumina – 9% residue – 2% stocks) | Output: 3,28 Mtonnes of Alumina (total outputs: 81% Alumina – 8% residue – 11% stocks)

## Slide 18: Comparison of Aluminium production in 2017 (China / Europe)
Quantification
http://www.world-aluminium.org/statistics/massflow/
China | Europe
Production inputs: 47,2 Mtonnes (77,3% local Aluminia – 20,1% local scrap – 2,6% import scrap) | Production inputs: 10,0 Mtonnes (50,2% local scrap – 26,2% import Aluminia – 21,5% local Aluminia - others)
Production output: 35,9 Mtonnes of primary Aluminium (77,4%) 10,5 Mtonnes of Recycled Aluminum (22,6%) (93,6% domestic – 1% export – 5,4% stocks & others) | Production output: 4,1 Mtonnes of primary Aluminium (46,1%) 4,8 Mtonnes of Recycled Aluminum (53,9%) (98,7% domestic – 1,3% export – 2,4% stocks & others)
Ingots per capita: 3,56 kg | Ingots per capita: 3,00 kg

## Slide 19: Comparison of in-use stock and flows in 2017 (China / Europe)
Quantification
http://www.world-aluminium.org/statistics/massflow/
China | Europe
Use input: 28,7 Million tonnes (96% domestic – 4% import) | Use input: 12,1 Million tonnes (67% domestic – 33% import)
In-use stock: 235 Million tonnes (cars, building and construction etc.) Per capita: 165,6 kg/capita | In-use stock: 183 Million tonnes Per capita: 269,5 kg/capita
End-of-life products: 4,6 Mtonnes (75% old scrap recovered) | End-of-life products: 4,8 Mtonnes (79% old scrap recovered)
↘Trend: The net annual increase in Chinese in-use stocks is currently almost 4 times higher than that of Europe or North America

## Slide 20: Answer to the research question and conclusion (1/2)
Interpretation
“ The purpose of this study is the quantification of regional stocks and flows of rolled, extruded and casting alloys across space and over time, giving the industry the ability to evaluate the potential to recycle aluminium scrap most efficiently.”
1,1 billions of tonnes of primary Aluminium produced between 1950 & 2014
  860 million tonnes (78%) of which are still in-use
  80 million tonnes (~7%) are non-recycled products (post-use fate is not know)
  The remaining part is landfilled, incinerated or dissipated

## Slide 21: Answer to the research question and conclusions (2/2)
Interpretation
Aluminium Scrap recycling
Europe is net exporter of scrap (surplus scrap in Black)
China needs to import 4Mt/yr of scrap to avoid using primary metal (light grey)
Globally: recycled scrap reaches 11Mt/yr
This leaves a non-supplied recycled demand of 3Mt/year (light grey)

## Slide 22
❹ Perspectives & conclusions
  ̶̶ Other types of MFA according to OECD
  ̶ Other sustainability tools
  ̶ Summary of the lecture
Lecture (II): Procedure, Application & Perspectives

## Slide 23
MFA: a family of tools
Source: Measuring material flows & resource productivity. Volume I. The OECD Guide (2008).

## Slide 24
OCDE Top-Down Approach
Source: Measuring material flows & resource productivity. Volume I. The OECD Guide (2008).

## Slide 25: Example: economy-wide monitoring of the biophysical circular economy for Austria.

## Slide 26
❹ Perspectives & conclusions
  ̶̶ Other types of MFA according to OECD
  ̶ Other sustainability tools
  ̶ Summary of the lecture
Lecture (II): Procedure, Application & Perspectives

## Slide 27: Environmental Prioritization of Products (I/2)
Food, Mobility and Housing dominate (70 % of impacts at 50% expenditure)
Source: Journal Indust. Ecology 10:3 (2006)

## Slide 28: Environmental Prioritization of Products (2/2)
Source: Tukker et al. 2006.
Environmental Impact of Products (EIPRO
surface is a measure for priority
figure indicates if shift in expenditure makes environm. sense and if ‘rebounds’ are possible

## Slide 29: National level resource accounting: System for Environmental & Economic Accounts (SEEA)

## Slide 30: Integration of tools at various levels
Different system analytical tools and a consistent set of indicators are necessary to ensure innovation moves towards a sustainability
Questions at various levels
Macro
Meso
Micro
Indicators
Life Cycle Assessment
Tools available
Material Flow analysis
EE Input-Output tables
& Env. accounts
GDP, EF, etc.

## Slide 31
❹ Perspectives & conclusions
  ̶̶ Other types of MFA according to OECD
  ̶ Other sustainability tools
  ̶ Summary of the lecture
Lecture (II): Procedure, Application & Perspectives

## Slide 32: Examples of potential student projects
❶ Cobalt (Co) in the European value chain of electric mobility
❷ Machinery tools in the French economy – Focus on the Tungsten
❸ Supply of phosphate fertiliser: Potential of recycling from wastewater in Nouvelle Aquitaine region
Source: the Guardian
Source: Vadoudi et al. 2015

## Slide 33: Thanks for you attention
Prof. Guido Sonnemann ​
guido.sonnemann@u-bordeaux.fr​
CyVi​
Research group on Life Cycle Assessment & sustainable chemistry
Institut des Sciences Moléculaires - ISM​
Université de Bordeaux – UMR 5255 CNRS​
351 Cours de la libération – Bât A12​
33 405 TALENCE cedex – France​
Tél : 05 40 00 31 83​
Web : http://www.ism.u-bordeaux1.fr​